## Slide 1
A team can have up to 4 members including the team leader. Add rows if necessary.
DriftSense — Team Details
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
4
Member 3
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
Kaccha Mango
Abishek Guru M
4
Tejashwan Gangishetty
4
Anushka Chandergi
4
Meenakshi Sundaram
4
Vellore Institute of Technology, Vellore
9080439729
abishekguru.m2023@vitstudent.ac.in

## Slide 2
Problem Statement Addressed
Drift-Sense: AI-Powered Navigation-Error Recovery for Wafer Inspection Tools
DESCRIPTION / DETAILS
Inspection tools must relocate a previously captured 100x Reference to the same site in a wider, noisier 10x Search image — across a ~10:1 (9:1-11:1) scale gap, 1-2° rotation drift, and realistic SEM degradation.
Real DRAM structure is highly repetitive: a wrong periodic repeat can score almost identically to the true site. DriftSense recovers the target center (x, y) automatically, with a confidence/ambiguity score alongside it.

## Slide 3
Idea Description - Describe your Idea/Solution/Prototype
Provide a brief summary of your idea, including the key concept and approach. Provide a brief overview of your solution and how it addresses the problem statement.
KEY CONCEPT & APPROACH
Classical multi-scale, multi-rotation template matching: search scale x rotation hypotheses, rank candidates by normalized cross-correlation, then refine to sub-pixel precision.
SOLUTION OVERVIEW
Paired with DriftSense's own synthetic DRAM mat/strip generator (realistic macro-structure + SEM degradations), so the pipeline is built and evaluated against data that mirrors real repetitive-pattern ambiguity.

## Slide 4
Proposed Solution - Describe your Idea/Solution/Prototype
Describe your idea in detail. Include the methodology, technologies involved, and how it addresses the chosen problem statement.
SOLUTION DETAILS
Pipeline: Reference → candidate generation (ZNCC over a 9x9 grid of scale x rotation hypotheses, ±8% scale / ±5°) → dedup → ranking (highest-score match) → sub-pixel refinement → (x, y) + confidence/ambiguity score.
Data generator: DRAM mats rendered independently, tiled with strip/routing regions on a shared canvas — real structural boundaries, not an injected marker, disambiguate repeats; SEM degradations layered on after.
The hypothesis grid was widened from 5x5 to 9x9 (same span, finer step) after validation showed this recovers rotation/scale-drift failures without affecting unrelated cases.

## Slide 5
Innovation and Uniqueness
Highlight what makes your idea unique or innovative compared to existing solutions.
KEY INNOVATION
A physically-grounded synthetic DRAM generator: independently-rendered mats tiled with real strip/peripheral structure, not an injected disambiguation signal — combined with a validated multi-hypothesis scale/rotation search.
COMPETITIVE ADVANTAGE
Every candidate improvement (finer hypothesis grid, learned re-ranker, periodicity scoring, wider candidate pool) is tested against a mandatory integration gate on held-out and external data before being trusted — most were honestly rejected; one validated change shipped.

## Slide 6
Impact and Benefits
Explain how your solution will make an impact, such as improving performance, reducing costs, increasing efficiency, or solving other challenges.
Primary Impact
The classical pipeline localizes to sub-pixel accuracy on most pairs (median error 0.33px). A validated 9x9 hypothesis-grid search recovers many rotation/scale-drift failures a coarser 5x5 grid misses, without regressing any unaffected case.
Quantifiable Outcomes
71.2%@5px pooled (n=156). Mean error 65.3px → 53.6px. Candidate recall@5px 82.6% → 87.1%. Catastrophic (>50px) rate 18.6% → 16.7%. ~1.6s/pair on CPU. Periodic-pattern catastrophic failures remain a known, disclosed limitation.

## Slide 7
Feasibility, Technology & Next Steps
Software-only, CPU-capable, and fully reproducible — with links, references, and next steps below.
FEASIBILITY, LINKS & NEXT STEPS
Feasibility: pure Python/OpenCV/NumPy classical pipeline, CPU-only in production (~1.6s/pair); PyTorch used only for a rejected, non-production learned-reranker experiment.
GitHub: https://github.com/teja120805-cyber/Semicon-26---Kacha-Mango
Demo video: https://drive.google.com/drive/folders/1G6Wa_ILJXcvpa6gIHGHpws5hdlO48gVC?usp=sharing
References: Foi, Trimeche, Katkovnik & Egiazarian (2008) Poisson-Gaussian noise modeling; Orji et al. (2018) Nature Electronics metrology; Applied Materials/Hugging Face SEM reference generator (official starter resource).
Future work: periodicity-aware re-ranking with more data, richer spatial context, robustness to unseen acquisition conditions.
Python, OpenCV, NumPy
CPU-only, no GPU needed
PyTorch (experiments), Streamlit

## Slide 8
GitHub & Video Link
GitHub Repository
https://github.com/teja120805-cyber/Semicon-26---Kacha-Mango
Prototype / Simulation Video
https://drive.google.com/drive/folders/1G6Wa_ILJXcvpa6gIHGHpws5hdlO48gVC?usp=sharing

## Slide 9
Research and References
Research Background & Methodology
Briefly describe the research foundation or scientific principles supporting your idea.
{Detail your research findings, theoretical basis, or methodology here...}
References & Citations
List key papers, articles, or data sources.
{Ref 1: Title of Paper/Article - Source/URL}
{Ref 2: Title of Paper/Article - Source/URL}
{Ref 3: Title of Paper/Article - Source/URL}